## Slide 1: CSE 185 Introduction to Computer Vision
Light and color

## Slide 2: Light and color
Human eye
Light
Color
Projection
Reading: Chapters 2,6

## Slide 3: Camera aperture
f / 5.6 (large aperture)
f / 32 (small aperture)

## Slide 4: The human eye
The human eye is a camera
  Iris: colored annulus with radial muscles
  Pupil: the hole (aperture) whose size is controlled by the iris
  What’s the “film”?
    photoreceptor cells (rods and cones) in the retina
Notes: Note that the retina is curved

## Slide 5: Human eye
Retina: thin, layered membrane with two types of photoreceptors
  rods: very sensitive to light but poor spatial detail
  cones: sensitive to spatial details but active at higher light level
  generally called receptive field

## Slide 6: Human vision system (HVS)

## Slide 7: Exploiting HVS model
Flicker frequency of film and TV
Interlaced television
Image compression

## Slide 8: JPEG compression
Q=100 Compression ratio: 2.6
Q=50 Compression ratio: 15
Q=25 Compression ratio: 23
Q=10 Compression ratio: 46
Q=1 Compression ratio: 144
Uncompressed 24 bit RGB bit map: 73,242 pixels require 219,726 bytes (excluding headers)

## Slide 9: JPEG compression

## Slide 10: Digital camera
    http://electronics.howstuffworks.com/digital-camera.htm
CCD vs. CMOS
Low-noise images
Consume more power
More and higher quality pixels
More noise (sensor area is smaller)
Consume much less power
Popular in camera phones
Getting better all the time

## Slide 11: Color
What colors do humans see?
The colors of the visible light spectrum
color wavelength interval frequency interval
red ~ 700–635 nm ~ 430–480 THz
green ~ 560–490 nm ~ 540–610 THz
blue ~ 490–450 nm ~ 610–670 THz

## Slide 12: Color
Plot of all visible colors (Hue and saturation):
Color space: RGB, CIE LUV, CIE XYZ, CIE LAB, HSV, HSL, …
A color image can be represented by 3 image planes

## Slide 13: Bayer pattern
A practical way to record primary colors is to use color filter array
Single-chip image sensor: filter pattern is 50% G, 25% R, 25% B
Since each pixel is filtered to record only one color, various demosaicing algorithms can be used to interpolate a set of complete RGB for each point
Some high-end video cameras have 3 CCD chips
Color filter array

## Slide 14: Demosaicing
original reconstructed

## Slide 15: Demoasicing

## Slide 16: Demosaicing
How can we compute an R, G, and B value for every pixel?

## Slide 17: Color camera
Bayer mosaic color filter
CCD prism-based color configuration

## Slide 18: Grayscale image
Mainly dealing with intensity (luminance)
Usually 256 levels (1 byte per pixel): 0 (black) to 255 (white) (often normalized between 0 and 1)
Several ways to convert color to grayscale, e.g., Y=0.2126R+0.7152G+0.0722B

## Slide 19: Recolor old photos
http://twistedsifter.com/2013/08/historic-black-white-photos-colorized/

## Slide 20: Projection
See Szeliski 2.1

## Slide 21: Projection
Fun application
PhotoFunia

## Slide 22: Correspondence and alignment
Correspondence: matching points, patches, edges, or regions across images
≈

## Slide 23: How do we fit the best alignment?

## Slide 24: Common transformations
translation
rotation
aspect
affine
perspective
original
Transformed

## Slide 25: Modeling projection
The coordinate system
  We will use the pin-hole model as an approximation
  Put the optical center (Center Of Projection) at the origin
  Put the image plane (Projection Plane) in front of the COP
  The camera looks down the negative z axis
    we need this if we want right-handed-coordinates
Notes: This way the image is right-side-up

## Slide 26: Modeling projection
Projection equations
  Compute intersection with PP of ray from (x,y,z) to COP
  Derived using similar triangles
  We get the projection by throwing out the last coordinate:

## Slide 27: Homogeneous coordinates
Is this a linear transformation?
Trick: add one more coordinate:
homogeneous image
coordinates
homogeneous scene
coordinates
Converting from homogeneous coordinates
  no—division by z is nonlinear

## Slide 28: Perspective projection
Projection is a matrix multiply using homogeneous coordinates:
divide by third coordinate
This is known as perspective projection
  The matrix is the projection matrix

## Slide 29: Perspective projection
How does scaling the projection matrix change the transformation?

## Slide 30: Orthographic projection
Special case of perspective projection
  Distance from the COP to the PP is infinite
  Good approximation for telephoto optics
  Also called “parallel projection”: (x, y, z) → (x, y)
  What’s the projection matrix?
Image
World

## Slide 31: Orthographic projection variants
Scaled orthographic
  Also called “weak perspective”
  Affine projection
    Also called “paraperspective”

## Slide 32: Camera parameters
See MATLAB camera calibration example

## Slide 33: Camera parameters
Projection equation
  The projection matrix models the cumulative effect of all parameters
  Useful to decompose into a series of operations
projection
intrinsics
rotation
translation
identity matrix
A camera is described by several parameters
  Translation T of the optical center from the origin of world coords
  Rotation R of the image plane
  focal length f, principle point (x’c, y’c), pixel size (sx, sy)
  yellow parameters are called extrinsics, red are intrinsics
  The definitions of these parameters are not completely standardized
    especially intrinsics—varies from one book to another